## Slide 1: Information Security - 2
Topic: Architectural Aid to Secure Systems Engineering
V. Kamakoti
RISE LAB, Department of Computer Science and Engineering
IIT Madras
Session – 7: STRUCTURED COMPUTER ORGANIZATION

## Slide 2: Computer Organization
Computer Organization Vs Computer Architecture
Application Binary Interface (ABI)
  Compiler and Operating Systems interact with Architecture
  Compiler to Machine Language Translation
  Instruction Set Architecture (ISA) is crucial
Understand the Compiler-Architecture ABI

## Slide 3
Structured Computer Organization
Programming Language level
Assembly Language level
Operating Systems level
Microprogramming level
Digital Logic level
Computer
Architecture
Compilers ask
for features from the
Architecture to
induce more sophistication
in the Programming Languages
Compiled code/ Assembly code
Advanced Addressing modes
Sophisticated Instruction set
Support for Memory Management
and Task Management
Multiuser OS - Protection, Virtual
Memory, Context Switching
Intel
Understanding
How I manage
these demands makes my
biography
interesting

## Slide 4: Memory Management
Multi User Operating Systems
  Ease of Programming
  Process Mobility in the Address Space
  Multiprocess Context switching
  Protection across Processes
    Intra process protection: Separation of Code, Data and Stack
    Inter process protection
Virtual Memory
  4GB address space for every process
Ensured by
Segmentation
Ensured by
Paging

## Slide 5
if (j>k)
max = j
else
max = k
Code_Segment:
mov EAX, [0]
mov EBX, [4]
cmp EAX,EBX
jle 0x7 //Label_1
mov [8], EAX
jmp 0x5 //Label_2
Label_1: mov [8], EBX
Label_2: ….
Ease Of Programming
Data Segment:
0: // Allocated for j
4: // Allocated for k
8: // Allocated for max
Code and Data
segments are separate
and both assumed
to start from 0
Operating System
(Kernel)
Main Memory
Other User
Process
Our Code
Segment
Vacant
Space
Our Data
Segment
Vacant
Space
0000
0700
0900
1900
2100
2300
2500
Address of j: 2100
Address of k: 2104
Address of max: 2108
2100
Segment Register (Data)
Every Memory Data
Access should add
the value stored in
Data Segment Register
By default.

## Slide 6
if (j>k)
max = j
else
max = k
Code_Segment:
mov EAX, [0]
mov EBX, [4]
cmp EAX,EBX
jle 0x7 //Label_1
mov [8], EAX
jmp 0x5 //Label_2
Label_1: mov [8], EBX
Label_2: ….
Process Mobility
Data Segment:
0: // Allocated for j
4: // Allocated for k
8: // Allocated for max
Operating System
(Kernel)
Main Memory
Other User
Process
Our Code
Segment
Vacant
Space
Our Data
Segment
Vacant
Space
0000
0700
0900
1900
2100
2300
2500
Address of j: 2100
Address of k: 2104
Address of max: 2108
2100
Segment Register (Data)
A new process needs a
segment of size 260
The space is available
but not contiguous
Our Data
Segment
Vacant
Space
2300
New User
Process
2160
Vacant Space
Address of j: 2300
Address of k: 2304
Address of max: 2308

## Slide 7: End of Session-7 Thank You