## Slide 1: Information Security - 2
Topic: Architectural Aid to Secure Systems Engineering
V. Kamakoti
RISE LAB, Department of Computer Science and Engineering
IIT Madras
Session – 8: X86 ISA – Part 1

## Slide 2: CISC Vs RISC
X86 is CISC while ARM is RISC
CISC is Compiler’s heaven while RISC is Architecture’s heaven
Orthogonal ISA in RISC
  Fixed format that is easy to decode
Programming Language to Execution involves two levels of translation
  Compilation by compiler
  Interpretation by Instruction decoder

## Slide 3: Intel General Purpose Registers

## Slide 4: 64-bit and above Registers
RAX, RBX, RCX, RDX, RSI, RSP, RDI, RBP – 64 bit General purpose registers sharing space with its corresponding 32-bit registers
R8-R15, additional general purpose registers
  R8D – R15D (32 bit counter part)
  R8W – R15W (16 bit counter part)
ST0-ST7, 80 bit floating point
MMX0-MMX7, 64-bit multi media
XMM0-XMM7, 128-bit registers – used for floating point and packed integer arithmetic

## Slide 5: Intel Segment Registers

## Slide 6: Multiple Segments
The segment register can change its values to point to different segments at different times.
X86 architecture provides additional segment registers to access multi data segments at the same time.
  DS, ES, FS and GS
X86 supports a separate Stack Segment Register (SS) and a Code segment Register (CS) in addition.
By default a segment register is fixed for every instruction, for all the memory access performed by it. For eg. all data accessed by MOV instruction take DS as the default segment register.
An segment override prefix is attached to an instruction to change the segment register it uses for memory data access.

## Slide 7
Multiple Segments
DS
SS
ES
CS
0000
0500
1500
2500
3500
mov [10], eax
- this will move the contents of eax register to memory location 0510
Opcode: 0x89 0x05 0510
mov [ES:10], eax
this will move the contents of eax register to memory location 3510
Opcode
0x26 0x89 0x05 0510
“0x26” is the segment override prefix.

## Slide 8
Multiprocess Context switching
Process 1
CS
Process 1
DS
Process 2
CS
Process 2
SS
Process 2
DS
Process 1
SS
CS
DS
SS
Process 1 in Execution
Process 2
in
Execution

## Slide 9: Other System Registers
Control – CR0, CR2, CR3 (each 32-bits)
  CR0 is very important
    Bit 0 – PE bit – when set processor in protected mode else real mode
    Bit 3 – TS bit – The processor sets this bit automatically every time it performs a task switch. This can be cleared using a CLTS instruction
    Bit 31 – PG bit – when set paging MMU is enabled else it is disabled

## Slide 10: Other System Registers
Control – CR0, CR2, CR3 (each 32-bits)
  CR2 – Read only register – deposits the last 32-bit linear address that caused a page-fault
  CR3 – Stores the physical address of the PDB – Page Directory Base register. The paging tables are to be 4KB aligned and hence the 12 least significant bits are not stored and ignored

## Slide 11: Other System Registers
Debug Registers
  DR0, DR1, DR2, DR3, DR6, DR7
  DR0-DR3 can hold four linear address breakpoints so that if the processor generates these addresses a debug exception (Interrupt 1) is caused
  DR6 – Debug status register indicating the circumstances that may have caused the last debug fault
  DR7 – Debug control register. By filling in the various fields of this register, you can control the operation of the four linear address breakpoints

## Slide 12: End of Session-8 Thank You