## Slide 1: Information Security - 2
Topic: Architectural Aid to Secure Systems Engineering
V. Kamakoti
RISE LAB, Department of Computer Science and Engineering
IIT Madras
Session – 11: x86 memory segmentation

## Slide 2: Protection Implementation
Every segment is associated with a descriptor stored in a descriptor table.
The privilege level of any segment is stored in its descriptor.
The descriptor table is maintained in memory and the starting location of the table is pointed to by a Descriptor Table Register (DTR).
The segment register stores an offset into this table.

## Slide 3: Descriptor Tables
There are two descriptor tables
  Global Descriptor Tables
  Local Descriptor Tables
The global descriptor table’s base address is stored in GDTR
The local descriptor table’s base address is stored in LDTR
The two privileged instructions LGDT and LLDT loads the GDTR and LDTR.

## Slide 4: Structure of a Descriptor

## Slide 5: Updating Segment registers
Segment registers (DS, ES, SS, GS and FS) are updated by normal MOV instructions.
  MOV DS,0x10
The above command is successful if and only if the descriptor stored at the offset 0x10 in the descriptor table has a privilege level numerically greater than or equal to the CPL.
A process with CPL = 3 cannot load the segment descriptor of CPL <= 2, and hence cannot access the segments.

## Slide 6: Updating segment registers
The code segment register is updated by normal jump/call operations.
  jmp 0x20:0x1000
  This updates the CS by 0x20, provided the descriptor stored at offset 0x20 has a privilege level numerically greater than or equal to CPL
Other modes of updating CS register
  Numerically higher to lower Privilege Levels using CALL gates – useful for system calls.
  Any privilege level to any other privilege level using task switch.

## Slide 7: End of Session-11 Thank You