## Slide 1: Information Security - 2
Topic: Architectural Aid to Secure Systems Engineering
V. Kamakoti
RISE LAB, Department of Computer Science and Engineering
IIT Madras
Session – 12: process isolation through segmentation

## Slide 2: Descriptor Tables
There are two descriptor tables
  Global Descriptor Tables
  Local Descriptor Tables
The global descriptor table’s base address is stored in GDTR
The local descriptor table’s base address is stored in LDTR
The two privileged instructions LGDT and LLDT loads the GDTR and LDTR.

## Slide 3: Structure of a Selector
Index
T1
0
2
15
T1 = 0 GDT
= 1 LDT
Since segment descriptors are each 8 bytes, the last three bits of the selector is zero, in which one of them is used for LDT/GDT access.

## Slide 4
Two process each of PL = 3 should be allotted segments such that one should not access the segments of other.
GDTR
GDT
All descriptors in GDT have
PL = 0,1,2
LDTR
LDTR
Per process
Per process
If at all each process should access memory, it has to use the descriptors in its LDTR only and it cannot change the LDTR/LDT/GDTR/GDT contents as they would be maintained in a higher privileged memory area.

## Slide 5: Did You Note!!
There is an 100 % degradation in Memory access time – because every memory access is two accesses now, one for getting the base address and another for actually accessing the data.
A solution indeed: Along with the segment registers, keep a shadow registers which stores additional necessary information.

## Slide 6
Segment selector | Base Address, Limit, DPL.
Visible part
Hidden part
CS
SS
DS
ES
FS
GS

## Slide 7: Be Careful
0x10
20
120
Descriptor Table
Base Address
Linear Address
Logical Address
Base = 100
Changing Base
Linear address will still be 120
Have to execute
mov DS,0x10 again to get the answer as 220, as this would update the hidden part
Base = 200
add [DS:20],eax

## Slide 8: End of Session-12 Thank You