## Slide 1: Information Security - 2
Topic: Architectural Aid to Secure Systems Engineering
V. Kamakoti
RISE LAB, Department of Computer Science and Engineering
IIT Madras
Session – 13: PAGING AND VIRTUAL MEMORY

## Slide 2: Virtual Memory and Paging
It is always enough if the next instruction to be executed and the data needed to execute the same are available in the memory.
The complete code and data segment need not be available.
Use of paging to realize the stuff!
By using segmentation the processor calculates an 32-bit effective address.

## Slide 3: Paging fundamentals
Each page is 4096 bytes
Physical RAM has page frames like photo frames, which is also 4096 bytes.
A page is copied into the page frame, if needed and removed to accommodate some other page.
By this, a 4 GB code can run on a 128MB physical memory
This is also called demand paging.

## Slide 4: Paging Technique
Page Directory
Stored In RAM
(Location of every page in RAM if it is loaded, else INVALID)
32-bit Address
20-bit address
12-bit address
+

## Slide 5: Protected Mode Addressing with paging
DIR
TABLE
OFFSET
CR3 REG
DIR ENTRY
PG TBL ENTRY
PHYS ADDRS
PAGE DIRECTORY
PAGE TABLE
PAGE FRAME
12
10
10
4KB entries with 4 bytes per entry
4KB entries with 4 bytes per entry
If 20 bytes are used as a single level paging then page table alone is 4 MB which is inefficient. So two level paging.
Develop the page table on demand
TLB’s used to improve performance
Dirty bit accommodated in each page entry

## Slide 6: Protected Mode Addressing - Paging entries

## Slide 7: End of Session-13 Thank You