## Slide 1: Information Security - 2
Topic: Architectural Aid to Secure Systems Engineering
V. Kamakoti
RISE LAB, Department of Computer Science and Engineering
IIT Madras
Session – 15: memory segmentation deep dive – 1 (segment descriptors)

## Slide 2: Memory Segmentation
Segment Descriptors
  80886 to 80386+
    In 8086, the program is not expected to generate a non-existent memory address. If it does, then the processor shall try to access the same and read bogus data, or crash
    In 80386+ (and above) the segment attributes (base, limit, privilege etc) are programmable and no matter how privileged the code may be, it cannot access an area of memory unless that area is described to it.

## Slide 3: Insight into 80386+ segments
Segments are
  Areas of memory
  Defined by the programmer
  Used for different purposes, such as code, data and stack
Segments are not
  All the same size
  Necessarily paragraph aligned
  Limited to 64KB

## Slide 4: Structure of a Descriptor

## Slide 5: Segment Descriptors
Describes a segment using 64-bits (0-63)
Must be created for every segment
Is created by the programmer
Determines a segment’s base address (32-bits) (Bits 16-39, 56-63)
Determines a segment’s size (20-bits) (Bits 0-15, 48-51)

## Slide 6: Segment Descriptors (Cont’d)
Defines whether a segment is a system segment (=0) or non-system (=1) (code, data or stack) segment (System bit) (Bit 44)
Determines a segment’s use/type (3-bits) (Bits 41-43) after the above classification
Determines a segment’s privilege level (2 bits) (Bits 45-46) – DPL (Descriptor Privilege Level) Bits

## Slide 7: Segment Descriptor (Cont’d)
Accessed (A)-bit: Bit 40, automatically set and not cleared by the processor when a memory reference is made to the segment described by this descriptor.
Present (P)-bit: Bit 47, indicates whether the segment described by this descriptor is currently available in physical memory or not.
Bits 40-47 of the descriptor is called the Access Right Byte of the descriptor.
User (U)-bit and X bit: Bit 52 (U-bit) not used and Bit 53 (X-bit) reserved by Intel

## Slide 8: Segment Descriptor (Cont’d)
Default size (D)-bit: Bit 54, when this bit is cleared, operands contained within this segment are assumed to be 16 bits in size. When it is set, operands are assumed to be 32-bits.
Granularity (G)-bit: Bit 55, when this bit is cleared the 20-bit limit field is assumed to be measured in units of 1byte. If it is set, the limit field is in units of 4096 bytes.

## Slide 9: Types of non-system segment descriptors
System bit S = 1
  000 – Data, Read only
  001 – Data, Read/Write
  010 – Stack (expand down), Read only
  011 – Stack (expand down), Read/Write
  100 – Code, Execute only
  101 – Code, Execute/Read
  110 – Conforming Code, Execute only
  111 - Conforming Code, Execute/Read

## Slide 10: D-bit for different descriptors
Code segment
  D = 0 then 16-bit 80286 code
  D = 1 then 32-bit 80386+ code
Stack Segment
  D = 0 then stack operations are 16-bit wide, SP is used as a stack pointer, maximum stack size is FFFF (64 KB)
  D = 1 then stack operations are 32-bit wide, ESP is used as a stack pointer, maximum stack size is FFFFFFFF (4 GB)

## Slide 11: G-bit for descriptors
  G = 0 then a limit field in descriptor of value p indicates we can access p-1 bytes from base
  G = 1 then a limit field in descriptor of value p indicates we can access (p * 4096) - 1 bytes from base

## Slide 12: Stack/expand down segments
All offsets must be greater than limit.
In stack descriptor, D and G bits are to be the same, else contradiction.
Base
FFFF
Addressable area
Base
FFFF
Addressable area
Stack/expand-down
Non-stack
Limit
Limit

## Slide 13: End of Session-15 Thank You